## Slide 1: e-P10 - HARD GAS PERMEABLE LENSES FITTING IN KERATOCONUS, LONG TERM FOLLOW UP SHAHTALEBI M., JAFARZADEHPUR E.*, MIRZAJANI A. School of rehabilitation science, Iran University of Medical Sciences,, Tehran, IRAN
E-poster not available,
See the next page, to consult the corresponding abstract

## Slide 2
Purpose: To evaluate the influence of rigid gas-permeable contact lenses on corneal curvature and visual acuity in patients with keratoconus
Materials and Methods: Inten years follow up of 680 eyes from 341 patients with diagnostic keratoconus complete ophthalmologic examination, including manifest refraction, best spectacle visual acuity (BSCVA), bio microscopy, and corneal keratometry was performed. Then, trial R.G.P lenses (Flourex, wholk, Boston) were selected based on the flat sim K-reading and an apical touch fitting approach. Over contact lens refraction and best – corrected R.G.P visual acuities (RGP V.A) were recorded in minimum angle resolution (log M.A.R).
Results: The mean age of subjects was (±SD)23.58(±7/30) years. The mean visual acuity in right eye and left eye respectively in first visit without correction were 0.5 ± 0.1and 0.5 ± 0.11 (log M.A.R), The mean visual acuity in right eye and left eye respectively in last visit without correction were 0.48 ± 0.08 and 0.49 ± 0.09 (log M.A.R). Obviously, visual acuity with lenses was normal. The mean K-reading in both eye significantly flattened (P<0/01). in right eye changed from 6.69 mm±0.48 to 6.77 mm ± 0.49, for the left eye it changed from 6.72 mm ±0.56 to 6.75 mm ±0.61.
Conclusion: Corrected visual acuity and changes the optical and structural the keratoconic corneas could occur after wearing rigid gas-permeable contact lens. An appropriate fitting and corrected using lenses could have been controlled and stopped the disease.