## Slide 1: VISUAL OUTCOMES OF “ORBIFLEX K” LENSES IN PATIENTS WITH KERATOCONUS
1Berkay Akmaz, MD
2Ayse Yesim Oral, MD
2Baran Kandemir, MD
1Department of Ophthalmology, Katip Celebi Universty, Ataturk Education and Research Hospital, Izmir, Turkey
2Department of Ophthalmology, Dr. Lutfi Kirdar Kartal Training and Research Hospital, Istanbul, Turkey

## Slide 2: Purpose:
To evaluate the outcomes of Orbiflex K® (SwissLens SA, Prilly, Switzerland) contact lenses in visual rehabilitation of patients with keratoconus.

## Slide 3: Materials and Methods
Orbiflex K® (SwissLens SA, Prilly, Switzerland) rigid gas permeable (RGP) lenses were made of Boston XO (Hexafocon A) material. Geometrically, anterior and posterior optic zones are spherical. Peripherally, it has spherical structure with 3 basic curves (Figure 1). Dk/t value is equal to 100. Posterior surface basic curves range from 5.50 mm to-7.50 mm, in 0.10 mm intervals), lens diameter is from 8.70 to 9.20 mm in 0.10 mm steps. Posterior vertex power is found up to 40D with 0.25 intervals.
Figure 1: Orbiflex K lens geometry

## Slide 4: Methods:
This study included 80 eyes of 52 patients who admitted to eye clinic at Dr. Lütfi Kırdar Kartal Training and Research Hospital between November 2012 and December 2013 with a diagnosis of keratoconus. All patients received rigid contact lens prescription and followed up by 12 months. The mean age of patients was 26.1±6.9 (range, 15-43) years.
Patients were grouped according to Amsler-Krumeich classification staging by using keratometric values. Group 1 consisted of 12 eyes with stage 1. Group 2 consisted of 40 eyes with stage 2. Group 3 consisted of 10 eyes with stage 3, whereas Group 4 consisted of 18 eyes with stage 4. Uncorrected visual acuity (UCVA), best-corrected visual acuity (BCVA), subjective refraction, corneal topography, keratometry, central corneal thickness (CCT) measurements and biomicroscopic examination were performed for all eyes before and after contact lens.

## Slide 5: Results:
The mean value of flat meridian (K1) was 50.25±4.17 Dioptre (D), whereas the mean vertical meridian (K2) was 53.82±4.81D. The mean K value was 52.03±4.42D. The mean UCVA was 1.31±0.21 logMAR (Snellen 0.05±0.04). The mean values of BCVA with spectacle and contact lens were 0.79±0.33 logMAR (Snellen 0.21±0.17) and 0.05±0.08 logMAR (Snellen 0.91±0.13), respectively. Visual acuities were compared before and after contact lens and the differences were statistically significant (p<0.001). The mean line increases for Stage 1, 2, 3, and 4 keratoconus groups were 5.18±1.38 (range= 2-8), 5.86±1.79 (range= 2-8), 6.32±2.16 (range= 3-9), and 6.92±2.35 (range= 3-9) lines, respectively.

## Slide 6: Conclusion:
Orbiflex K lens provided significant visual improvement in patients with keratoconus at all stages of the disease.