## Slide 1
Author E-mail: drfcabib@mps.com.br
FINALITIES OF THE CORNEAL ENDOTHELIAL EXAMINATIONS IN CONTACT LENSES WEARERS - A CRITICAL STUDY -
Fernando Cesar Abib, MD, PhD *
Federal University of Paraná
Hospital Erasto Gaertner, Brazil
Dulcemar Szeremeta Abib, MD
Federal University of Paraná, Brazil
Eposter 78
Notes: 1

## Slide 2: Purpose
  To know the viability to perform the Specular Microscopy (SM) in Contact Lenses wearers during the clinical follow-up with 3 different finalities: Triage, endothelial diagnosis and research.

## Slide 3
Methods
103 SM of the right eyes of the contact lenses wearers;
Bio-Optics specular microscope and Bambi 2000 Plus software were used;
The Specular Microscopies were analyzed by the Reliability Indexes (RI) calculated by the CELLS ANALYZER - Corneal Endothelial Statistical Lab Patented with the results of the Specular Microscopy examinations. The relative error is called sample error (SE);
There are 3 different finalities to perform the Specular Microscopy:
  Triage Finality ;
  Endothelial Diagnosis Finality ;
  Research Finality ;
There are 3 different statistical power to calculate the endothelial sample size - Counted cell number per examination:
  90 % Reliability Degree (RD) and 10% Relative Error (RE)(SE).
  95% Reliability Degree (RD) and 5% Relative Error (RE) (SE).
  99% Reliability Degree (RD) and 1% Relative Error (RE) (SE).
All Specular Microscopy were analyzed as follow:
  Counted cell number (CCN) X Calculated sample size (CSS):
    CCN ≥ CSS, the SM is considered statistically representative of the endothelial cell population;
    CCN ≤ CSS, the SM is not considered statistically representative of the endothelial cell population.

## Slide 4: Results
90% RD and 10% SE: It is not accepted by the medical science
Sample size range: 12 - 71 cells and the average 27±11 cells;
SE range: 2.1% - 4.9% and average 3.38±0.58;
All the SM had planned sample error (10%) larger than the calculated sample error which determines, statically, the correct sample size for triage. 95% RD and 5% SE: It is accepted by the medical science
Sample size range: 65 - 389 cells and the average 148±60 cells;
SE range: 1.79% - 4.18% and average 2.18±0.48;
All the SM had planned sample error (5%) larger than the calculated sample error which determines, statically correct sample size endothelial diagnosis finality. To perform theses examinations were necessary from 2 to 10 different images. 99% RD and 1% RE: It is accepted by the medical science but impossilble to be performed
Sample size range: 2775 - 15897 cells and the average6240±2427 cells;
SE range: 2.77% - 6.46% and average 4.43±0.77;
All the SM had planned sample error (1%) smaller than the calculated sample error; determines, statically, incorrect sample size. It is impossible to acquire a very large different image number using the actual technology of Specular Microscopes.

## Slide 5: Conclusion
All the Specular microscopes can be used for triage finality;
Adopting 95% Reliability Degree and 5% Sample Error for Specular Microscopy it is possible to perform the examination with endothelial diagnosis finality if all the cells included in a specific number of different endothelial images are considered;
Adopting 99% Reliability Degree and 1% Sample Error for Specular Microscopy it is impossible to perform the examination with research Finality because it is impossible to acquire a very large number of different endothelial images with actual technology of Specular Microscopes;
We strongly suggest, for Research Finality, that the Specular Microscopy adopts 95% Reliability Degree and 5% Sample Error.