## Slide 1: Irregular corneas – K readings from four different devices
Vânia Lages, João Coelho, Carolina Abreu, David Dias, Maria João Furtado, Irene Barbosa
Ophthalmology Department of Centro Hospitalar do Porto | Director of Department: Dr. Pedro Menéres
Introduction
Purpose
To compare keratometry readings of patients with irregular cornea obtained from four different devices: Javal manual keratometer (JK) (Haag-Streit), Pentacam HR (Oculus), Orbscan IIz (Bausch & Lomb) and Kerato-refractometer (KR) (Oculus Park 1).
Material and methods
Design: Cross-sectional study.
Setting: Contactology Unit of the Ophthalmology Department of Centro Hospitalar do Porto, Porto, Portugal.
Study population: 64 eyes of forty-two patients with irregular cornea referred to Contactology Unit for contact lens fitting. Keratometry readings were obtained for each patient at the same visit with, at least, two different devices: JK, Pentacam, Orbscan and KR.
Main Outcome: Comparison of keratometry readings among the different devices. Steep (Ks) and flat keratometry (Kf) readings were recorded in diopters (D) for each eye and thereafter analysed.
Statistical analysis: Values are presented as arithmetic mean and standard error of mean, unless otherwise specified. The normality of data distribution was assessed using the Kolmogorov–Smirnov test. Student’s t test and ANOVA repeated measures, or other correspondent nonparametric test, were used, when appropriate for comparison between groups. Data analysis was performed using SPSS 20th edition. A P-value <0.05 was accepted as statistically significant.
Precise evaluation of corneal shape is useful over a range of clinical applications1-12, namely for contact lens fitting4,7. There are several commercially available devices to perform keratometry readings, with different methods of assessment, which have been extensively evaluated for reproducibility and inter-device agreement in normal cornea1,3-7,10-12. However, there is still a lack of knowledge in regard to the use of these devices in irregular cornea1,3,14.

## Slide 2: Irregular corneas – K readings from four different devices
Vânia Lages, João Coelho, Carolina Abreu, David Dias, Maria João Furtado, Irene Barbosa
Ophthalmology Department of Centro Hospitalar do Porto | Head of Department: Dr. Pedro Menéres
Results
64 eyes, of 42 patients, were analyzed. 56,3% were male patients and 47,3% female patients. The mean age was 34 years old, ranging from 13 to 75. The irregular cornea were due to keratoconus with no prior surgery in 50% of the eyes, intrastromal rings in 26,6%, penetrating keratoplasty in 17,2%, anterior lamelar keratoplasty in 3,1% and post-LASIK corneal ectasia in 3,1%.
K-readings with the four devices were performed on 15 eyes, the mean values with standard deviations for steep and flat keratometry are presented in Table 1 a, JK and Orbscan were performed on 34 eyes ( b ), JK and Pentacam were performed on 30 eyes ( c ), JK and KR on 23 eyes ( d ), Orbscan and Pentacam in 47 eyes ( e ), Pentacam and KR on 35 eyes ( f ) and Orbscan and KR on 35 eyes ( g ).
 |  | Javal | Pentacam | Orbscan | Kerato-refractometer | T-test P value | ANOVA P-value
a | Kflat | 44,88 ± 2,81 | 45,32 ± 3,46 | 45,79 ± 3,63 | 45,58 ± 3,56 |  | 0.526
 | Ksteep | 48,79 ± 4,33 | 48,57 ± 4,33 | 49,45 ± 4,51 | 48,86 ± 4,24 |  | 0,104
b | Kflat | 45,31 ± 4,33 |  | 45,21 ± 4,36 |  | 0,816 | 
 | Ksteep | 49,75 ± 4,45 |  | 50,47 ± 4,96 |  | 0,096 | 
c | Kflat | 45,63 ± 4,14 | 45,54 ± 4,19 |  |  | 0,845 | 
 | Ksteep | 50,16 ± 4,57 | 49,85 ± 4,21 |  |  | 0,421 | 
d | Kflat | 45,69 ± 3,44 |  |  | 46,17 ± 3,69 | 0,314 | 
 | Ksteep | 49,67 ± 3,89 |  |  | 49,98 ± 4,17 | 0,403 | 
e | Kflat |  | 45,52 ± 4,29 | 45,56 ± 4,06 |  | 0,873 | 
 | Ksteep |  | 49,57 ± 4,30 | 49,91 ± 4,78 |  | 0,293 | 
f | Kflat |  | 45,43 ± 4,12 |  | 45,73 ± 4,08 | 0,31 | 
 | Ksteep |  | 49,06 ± 4,48 |  | 49,49 ± 4,60 | 0,14 | 
g | Kflat |  |  | 46,25 ± 4,03 | 46,26 ± 4,25 | 0,964 | 
 | Ksteep |  |  | 50,07 ± 4,71 | 49,86 ± 4,28 | 0,497 | 
h | Kflat |  | 46,65 ± 3,88 | 46,01 ± 4,04 |  | 0,161 | 
 | Ksteep |  | 49,60 ± 4,83 | 49,79 ± 5,05 |  | 0,293 | 
i | Kflat |  | 44,15 ± 4,38 | 44,84 ± 4,05 |  | 0,037* | 
 | Ksteep |  | 49,42 ± 3,90 | 49,88 ± 4,68 |  | 0,177 | 
Table 1 - Mean and standard deviation of keratometry values and statistical analysis. (* statistically significant) |  |  |  |  |  |  | 

## Slide 3: Irregular corneas – K readings from four different devices
Vânia Lages, João Coelho, Carolina Abreu, David Dias, Maria João Furtado, Irene Barbosa
Ophthalmology Department of Centro Hospitalar do Porto | Head of Department: Dr. Pedro Menéres
Results
We found no statistically significant difference in the Ks and Kf readings among the four instruments and between the considered pairs of devices (b, c, d, e, f and g).
We also analyzed the keratometry readings obtained with Pentacam and Orbscan of two subgroups of patients, 22 eyes with keratoconus with no prior surgery and 23 eyes with keratoconus after surgery (penetrating keratoplasty and intrastromal rings). There was no statistically significant difference in the K readings from the two devices of the eyes with keratoconus ( h ) and there was a statistically significant difference in the Kf of postoperative eyes (p<0,04) but not in the Ks ( i ).
 |  | Javal | Pentacam | Orbscan | Kerato-refractometer | T-test P value | ANOVA P-value
a | Kflat | 44,88 ± 2,81 | 45,32 ± 3,46 | 45,79 ± 3,63 | 45,58 ± 3,56 |  | 0.526
 | Ksteep | 48,79 ± 4,33 | 48,57 ± 4,33 | 49,45 ± 4,51 | 48,86 ± 4,24 |  | 0,104
b | Kflat | 45,31 ± 4,33 |  | 45,21 ± 4,36 |  | 0,816 | 
 | Ksteep | 49,75 ± 4,45 |  | 50,47 ± 4,96 |  | 0,096 | 
c | Kflat | 45,63 ± 4,14 | 45,54 ± 4,19 |  |  | 0,845 | 
 | Ksteep | 50,16 ± 4,57 | 49,85 ± 4,21 |  |  | 0,421 | 
d | Kflat | 45,69 ± 3,44 |  |  | 46,17 ± 3,69 | 0,314 | 
 | Ksteep | 49,67 ± 3,89 |  |  | 49,98 ± 4,17 | 0,403 | 
e | Kflat |  | 45,52 ± 4,29 | 45,56 ± 4,06 |  | 0,873 | 
 | Ksteep |  | 49,57 ± 4,30 | 49,91 ± 4,78 |  | 0,293 | 
f | Kflat |  | 45,43 ± 4,12 |  | 45,73 ± 4,08 | 0,31 | 
 | Ksteep |  | 49,06 ± 4,48 |  | 49,49 ± 4,60 | 0,14 | 
g | Kflat |  |  | 46,25 ± 4,03 | 46,26 ± 4,25 | 0,964 | 
 | Ksteep |  |  | 50,07 ± 4,71 | 49,86 ± 4,28 | 0,497 | 
h | Kflat |  | 46,65 ± 3,88 | 46,01 ± 4,04 |  | 0,161 | 
 | Ksteep |  | 49,60 ± 4,83 | 49,79 ± 5,05 |  | 0,293 | 
i | Kflat |  | 44,15 ± 4,38 | 44,84 ± 4,05 |  | 0,037* | 
 | Ksteep |  | 49,42 ± 3,90 | 49,88 ± 4,68 |  | 0,177 | 
Table 1 - Mean and standard deviation of keratometry values and statistical analysis. (* statistically significant) |  |  |  |  |  |  | 

## Slide 4: Irregular corneas – K readings from four different devices
Vânia Lages, João Coelho, Carolina Abreu, David Dias, Maria João Furtado, Irene Barbosa
Ophthalmology Department of Centro Hospitalar do Porto | Head of Department: Dr. Pedro Menéres
References
Clinicians rely on their keratometers to provide precise information, especially when facing patients with irregular cornea5,7,8,15. Studies evaluating reproducibility and inter-device agreement for keratometry in irregular cornea are scarce1,3,14. In the study by Hashemi et al.14, he reports acceptable agreement between five different devices (Javal, Topcon automated kerato-refractometer, IOLMaster, EyeSys Corneal Analysis System, and Pentacam) in keratoconus patients, but in cases with Ks reading greater than 55.0D, he reported all devices had reduced reproducibility. A study by Thebpatiphat et al.16, reported the accuracy of keratometry significantly decreased as the severity of keratoconus increased. In our study, we found acceptable inter-device agreement. One of the main limitations of the study is the lack of evaluation of intra and inter-observer reproducibility of the measures obtained with each device. Also, because the true curvature of each participant cornea is not known, it is not possible to conclude which device is the most accurate. Another important limitation is the fact that our keratometry values were mainly below 55 diopters.
Discussion
Kawamorita T, et al, Repeatibility, reproducibility, and agreement characteristics of rotating Scheimpflug photography and scanning-slit corneal topography for corneal power measurement. J Cataract Refract Surg 2009; 35:127-133.
Yazici, AT et al, Measurements of anterior segment parameters using three different non-contact optical devices in keratoconus patients. Int J Ophthalmol, 2003;6(4):521-525.
Mehravaran S, Asgari S, Bigdeli S, Shahnazi A, Hashemia H (2014) Keratometry with five different techniques: a study device repeatability and inter-device agreement. INT ophtalmol 34:869-875
Tajbakhsh Z, Salouti R, Nowroozzadeh MH, Aghazadeh-Amiri M, Tabatabaee S & Zamani M. Comparison of keratometry measurements using the Pentacam HR, the Orbscan IIz, and the TMS-4 topographer.Ophthalmic Physiol Opt2012,32, 539–546.
Hidalgo IR et al, Repeatability and Inter-device Agreement for Three Different Methods of Keratometry: Placido, Scheimpflug, and Color LED Corneal Topography. J Refract Surg.2015;31(3):176-181.
Shirayama M et al, Comparison of Corneal Powers Obtained from 4 Different Devices. Am J Ophthalmol. 2009 Oct;148(4):528-535.e1.
Cho, P et al. The performance of four different corneal topographers on normal human corneas and its impact on orthokeratology lens fitting. Optometry and vision science. Volume 79, Issue 3, 175-183
Naderan M, Shoar S, Naderan M, Kamaleddin MA, Rajabi MT. Comparison of corneal measurements in keratoconic eyes using rotating Scheimpflug camera and scanning-slit topography. Int J Ophthalmol 2015;8(2):275-280.
Quisling S, Sjoberg S, Zimmerman B, Goins K. Comparison of Pentacam and Orbscan IIz on posterior curvature topography measurments in keratoconus eyes. American Academy of Ophthalmology 2006;113:1629-1632
Gonen T et al, Comparison of Keratometric Data Obtained by Automated Keratometer, Dicon CT 200, Allegro Topolyzer, and Pentacam J Refract Surg. 2012;28(8):557-561.
Whang WJ, Byun YS, Joo CK. Comparison of refractive outcomes using five devices for the assessment of preoperative corneal power. Clinical and Experimental Ophthalmology 2012;40:425-432.
Crawford AZ, Patel DV, Mcghee CNJ. Comparison and repeatability of keratometric and corneal power measurements obtained by Orbscan II. Am J Ophthalmol 2013;156:53–60.
Douthwaite WA, Mallen E. Cornea measurement comparison with Orbscan II and EyeSys Videokeratoscope. Optometry and Vision Science 2007;84(7):598-604
Hashemi H, Yekta A, Khabazkhoob M, Effect of keratoconus grades on repeatability of keratometry readings: Comparison of 5 devices. J Cataract Refract Surg 2015; 41:1065–1072
Lekhanont K, Nonpassopon M, Wannarosapark K, Chuckpaiwong V (2015) Agreement between Clinical History Method, Orbscan IIz, and Pentacam in Estimating Corneal Power after Myopic Excimer Laser Surgery. PLoS ONE 10(4): e0123729.
Thebpatiphat N, Hammersmith KM, Rapuano CJ, Ayres BD, Cohen EJ (2007) Cataract surgery in keratoconus. Eye Contact Lens 33:244–246